## Slide 1
CONVENTION AND EXHIBITION CENTRE, DUQM –
CONCEPTUAL SCHEME
June 2022

## Slide 2
Contents
Introduction
Site Context
Masterplan
Access Plan
Circulation layout
References for circular Convention Centre
Layouts
Elevations
Sections
Seat staging
Parking/toilet/fire exits Calculation
Area Calculation
3D Visualization
References

## Slide 3
Introduction
Public Authority for Special Economic Zones and Free Zones (OPAZ) has proposed 1000seater Convention and Exhibition centre at Duqm. This Project is located in the Governorate of Duqm of the Al Wusta Region, near Crown plaza hotel Duqm
The proposed facility has been designed as a spacious, modern and eco-friendly facility spread over a built-up area of 6000sqm. The facility has a capacity to host 1000 guests together and is equipped with state-of-the-art features and facilities like Multipurpose Hall of 1000seating capacity, Cafeteria of 75-100persons capacity, Multi-function lobby for exhibition and gathering spaces, a business centre with Conference and meeting rooms facilities (100capacity in total), Office for Administration staff, prayer rooms and other support facilities required for the smooth function of the proposed centre. Other facilities include Utility Buildings, Guard Room, and 100+ parking spaces with external development and Landscaping spreading over a developable area of around 19,000sqm.
The Convention building has been designed for two floors. The ground floor houses a state of the art, 1000seater multipurpose hall with roof height of 14m. This large spacious hall can be used for conventions, exhibition, auditorium like events, banquets etc; supported by spacious double height lobbies, cafeteria, prayers room, restrooms, a well-equipped stage and backstage facilities.
The mezzanine floor comprises of the office for administrative staff, and a well-equipped business centre, with 2 conference halls, meeting room, breakout space, reception and relevant support facilities.
The proposed Building has been designed keeping in mind a fast paced construction and a stringent time-line of 4months to completion and handing over. The building carcass has been designed for modular and prefabricated construction in steel, to be fit out and assembly based. The building is wrapped with modular panels of glass, GRC and concrete, with a Standing seam roof over the Hall and RCC slab over the mezzanine. The roof can also accommodate solar panels as an alternate source of energy.
The proposed 1000seater Convention and Exhibition centre at Duqm shall be a landmark for Al Wusta Region and a symbol of collaborative efforts between client and the contractor..

## Slide 4
Site Context
Park Inn by Radisson Hotel
Duqm Frontier Town
Crowne Plaza, Duqm
600 M
650 M
700 M
650 M
Land parcel (under consideration)
N

## Slide 5
Proposed Site
Proposed development Area = 19300 sq.m.
Land parcel for Convention Centre
Approach road
N

## Slide 6
Views

## Slide 7
Master Plan
Land parcel for Convention Centre
1
2
2
3
3
3
3
3
3
4
4
4
4
4
3
3
3
3
3
3
Convention Centre
Utilities
Landscape area
Parking area
1
2
3
4
Entry
Exit
Access Road
Key Plan
N

## Slide 8
Land parcel for Convention Centre
Entry
Exit
Access Road
Key Plan
N
Access Plan
Main Entrance for Convention Centre
VIP Entry
Staff Entry
Service Entry
Cafeteria Entry
Backstage Entry

## Slide 9
`
Entry
Exit
N
Access Plan
Main Entrance for Convention Centre
VIP Entry
Staff Entry
Service Entry
Cafeteria Entry
Backstage Entry
6.0m wide Driveway
6.0m wide Driveway
6.0m wide Driveway
7.5m wide Driveway
7.5m wide Driveway

## Slide 10
Circulation Layout
`
Entry
Exit
Fire tender movement
Vehicular access towards parking
Vehicular Drop-off(for public vehicles)
Service entry
N

## Slide 11
References for circular Convention Centre

## Slide 12
Views

## Slide 13
Ground Floor Plan
Activity areas
Utility/Services
Entrances / porch airlock lobby
Auditorium Hall
Green Rooms
Cafeteria & kitchen
Circulation area, staircase, lifts
Landscaping
1
2
2
3
3
4
4
5
6
7
1
2
3
4
5
6
7
3
Lobby area
Prayer room
Lounge
Air lock passage
Furniture store
Backstage rehearsal
Registration
Entry/Exits to the Auditorium Hall
Staff entry
Backstage entry
Service entry
Cafeteria entry
Main entry
Hall foyer
Stage
N
VIP entry

## Slide 14
Mezzanine Floor Plan
Activity areas
Utility/Services
Auditorium
Circulation area
Landscaping
1
2
3
4
5
6
7
Projection room
Conference room
Reception
Meeting room
Pantry
Manager room
Office
Rooms
8
1
2
2
3
4
4
5
5
7
6
8
8
8
3
Lobby
N

## Slide 15
Roof Plan
Aluminium standing seam roof
Canopy
RCC slab with solar farm
N

## Slide 16
Front Elevation
GROUND FLOOR LVL.
FIRST FLOOR LVL.
TERRACE LVL.
ROOF LVL.

## Slide 17
Section A
TERRACE LVL.

## Slide 18
Section B

## Slide 19
Seat staging
Option – 1 Flat seating

## Slide 20
Seat staging
Option – 2 Tier seating with Retractable Seating System
Flat floor of the Hall could also have a retractable seating system, a seating solution that converts the flat floor into a seating space, thus allowing flexibility. Retractable seating has fold down chairs that can be closed and opened (fully or partially) and stacked aside. Fold away auditorium seating is an efficient, space-saving way to provide seating on demand.

## Slide 21
Seat staging – Retractable Seating System (Optional)

## Slide 22
Toilet, Parking, Fire Exits Calculation for 1000 seater Convention Centre

## Slide 23
Area Statement

## Slide 24
Area Statement without airlock & reduced mezzanine

## Slide 25
Views

## Slide 26
Views

## Slide 27
Views

## Slide 28
References – façade treatment options
1. GRC Arabic pattern panel

## Slide 29
References – façade treatment options
Glass, Concrete panels and Screens

## Slide 30
References – façade treatment options
Glass reinforced Concrete (GRC) Cladding

## Slide 31
References – façade treatment options
Glass reinforced Concrete (GRC) Cladding

## Slide 32
References – façade treatment options
Glass reinforced Concrete (GRC) Cladding

## Slide 33
References – façade treatment options
Aluminium/ Galvalume Standing Seam roof and cladding

## Slide 34
References – façade treatment options
Metal. - Aluminium clad canopy

## Slide 35
References – façade treatment options
Solar Panels on the Roof

## Slide 36
Thank You